## Slide 1: Smarter restarts for a hard feed-blending problem
IA-2 · INTRODUCTION TO OPTIMIZATION TECHNIQUES
Recipe-Guided Iterated Local Search around SLP for the Fixed-Demand Pooling Problem
Group OPT-09 · Razzan Tambe (15) · Saurabh Tripathi (04) · Vivek Sharma (12)
Dept. of IT, K. J. Somaiya College of Engineering
Notes: Hello everyone. Our project is about a problem every feed mill has: mixing ingredients into animal feed at the lowest possible cost. In IA-1 we re-implemented a fast method from a research paper. In IA-2 we made that method more reliable. I will explain four things in simple steps: the problem, the weakness of today’s method, our fix, and the results.

## Slide 2: The problem: blending feed at the lowest cost
Raw materials
The ingredients. Each has a price and a nutrient content.
Mixing bins
A few shared mixes. Many products use the same bin.
Products
Each has a fixed tonnage and a minimum and maximum for every nutrient.
Some ingredients can also go straight into a product, at extra cost.
Goal: the lowest total cost of raw materials, with every product inside its nutrient limits.
Group OPT-09 · IA-2
2 / 13
Notes: Picture a feed mill. It buys raw ingredients, and each ingredient has a price and contains certain nutrients. The ingredients are first mixed into a few shared bins, and the bins are then blended into the final products, the different animal feeds. Every product must stay between a minimum and a maximum for each nutrient, and the mill must make a fixed amount of each product. Some ingredients can skip the bins and go straight into a product, but that costs extra. The goal is simple to say: spend as little as possible on ingredients while every product stays inside its limits.

## Slide 3: Why it is hard
THE CATCH
Product quality = bin share × bin quality
The bin quality depends on the bin recipe, and we choose the bin recipe too.
Unknown × unknown gives many “local best” answers.
THINK OF A HIKER IN FOG
Many valleys. Walking downhill stops in the nearest one, not always the deepest.
96
local best answers in a tiny example with only 2 nutrients
Mills re-solve this many times a day, so they need good recipes in seconds.
Group OPT-09 · IA-2
3 / 13
Notes: Why is this hard? A product’s quality depends on how much of each bin goes into it, which is the bin share, multiplied by the quality of that bin. But the bin’s quality depends on the bin recipe, which we also have to decide. So we are multiplying two unknowns, and that makes the problem “nonconvex”. In plain words: it has many “local best” answers. Imagine a hiker in fog who always walks downhill. They stop in the nearest valley, which may not be the deepest one. Even a tiny example with two nutrients has 96 such valleys. And mills solve this many times a day, so they need good answers in seconds, not hours.

## Slide 4: Today’s method and its weakness
HOW IT WORKS TODAY
1
Pick a random starting recipe.
2
Run SLP: small, safe steps downhill.
3
Repeat many times and keep the best.
Paper: 863× faster than FilterSQP and 20× faster than the global solver Baron.
RANDOM STARTS THAT END “GOOD”
6.4%
of runs on the 6 hard instances (paper: 14.8%). Good = feasible and within 0.2% of the best known cost.
Runs are independent: nothing is learned from earlier runs.
25–40% of runs on af-4, af-6-f and af-7 end infeasible: they break a limit.
Group OPT-09 · IA-2
4 / 13
Notes: Today’s best method is called SLP. At the current recipe it replaces the hard, curved part with a straight-line approximation, takes a small safe step, and repeats. It is very fast: the paper shows it is hundreds of times faster than other local solvers, and 20 times faster than the global solver Baron. But SLP only finds the nearest valley. So the standard approach is random restarts: start from many random recipes and keep the best result. We measured this with our IA-1 code. On the six hard instances, only 6.4 percent of random starts reach a good answer. Good means feasible and within 0.2 percent of the best known cost. The paper itself reports 14.8 percent. Two more problems: every restart is independent, so nothing is learned from earlier runs, and on three instances about a quarter to 40 percent of runs end infeasible, which means they break a limit.

## Slide 5: Our idea: three easy calculations
Ignore bin sharing
Diet LP
Each product gets its ideal cheapest recipe. This also gives a lower bound on the best cost.
Bin recipes fixed
Product LP
With the bin recipes fixed, the best product recipes are easy to find, and exact.
Bin shares fixed
Bin LP
With the bin shares fixed, the best bin recipes are easy to find. Alternating both LPs never raises the cost.
On af-1 the Diet LP bound (295.93) equals Baron’s 2-hour bound. LP = linear program: solved exactly and fast.
Group OPT-09 · IA-2
5 / 13
Notes: Here is our idea. The hard part of the problem is deciding the bin recipes. But notice: if somebody tells us the bin recipes, the rest of the problem becomes easy. It turns into a linear program, an LP, which a computer solves exactly and very fast. The same is true if somebody tells us how much of each bin goes into each product. So we use three LPs. The Diet LP ignores bin sharing and lets each product pick its ideal cheapest recipe. That gives us ideal recipes, and also a lower bound: no real solution can cost less than this. The Product LP fixes the bins and finds the best product recipes. The Bin LP fixes the bin shares and finds the best bin recipes. Switching between these last two never makes the cost worse. Important: we did not change the model or the SLP solver from IA-1. We only use these LPs around it. On the first instance, af-1, our bound matches the bound the global solver Baron needed two hours for, and we get it in milliseconds.

## Slide 6: The method in six steps
1
New
Ideal recipes
Diet LP: each product’s ideal recipe.
2
Modified
Smart start
Group similar recipes into starting bins.
3
New
Repair
Product and bin LPs make the start feasible.
4
Retained
Filter-SLP
The IA-1 solver, unchanged.
5
New
Polish
LPs clean up the end point. Never costlier.
6
New
Learn from the best
Nudge a bin, test 4 options, keep the best.
The first 3 runs, and any run after 6 without improvement, restart with a fresh smart start. One pass = one run; 20 runs per instance.
Group OPT-09 · IA-2
6 / 13
Notes: This is the whole method on one slide. Step 1: we solve the Diet LP for every product, which gives each product its ideal recipe. Step 2: we group similar ideal recipes using k-means, so products that want similar recipes share a bin. That gives a smart starting point instead of a random one. Step 3: we repair that start with the Product and Bin LPs until it is feasible. Step 4 is the SLP solver from IA-1, completely unchanged. Step 5: we polish its end point with the two LPs, and we only keep the result if it is feasible and cheaper. Step 6 is the learning part, and the next slide explains it. The tags show what is new, what we modified, and what we retained. After 3 fresh starts, later runs build on the best solution so far. If 6 runs in a row give no improvement, we do a fresh smart start again. One pass counts as one run, so the comparison with the baseline is fair.

## Slide 7: The smart move: learn from regret
1
Pick a product with high regret. It pays the most for sharing.
2
Pick a bin and blend its recipe toward that product’s ideal recipe.
3
Build 4 such candidates, repair each, and test each with a short 10-iteration SLP.
4
Continue the full SLP from the best candidate.
WHAT IS REGRET?
How much extra a product pays because it must share bins, compared with its own ideal recipe.
WHY TEST FIRST?
3 of 56
On af-3, only 3 of 56 possible moves escaped a stuck solution. A short SLP test ranked one of them first.
Group OPT-09 · IA-2
7 / 13
Notes: This is the part that makes the method learn. Regret means: how much extra does a product pay because it has to share bins, compared with the ideal recipe it would get on its own. A product with high regret is being served badly by the current bins. So we take the best solution found so far, pick a high-regret product, pick a bin, and blend that bin’s recipe toward the product’s ideal recipe. We build four such candidates, repair each one, and test each with a short ten-iteration SLP. Then we continue the full SLP from the best candidate. Why test first? On instance af-3, we once tried all 56 single moves from a stuck solution. Only 3 of them led to a good solution. The cost after repair did not show which ones, but a short SLP test ranked a good move first. So the test saves the full SLP for the promising moves.

## Slide 8: How we tested
11
feed-mill instances (af-series)
3 × 20
seeds × runs per instance
1,320
runs in total (+440 ablation)
Feasible
The run ends without breaking any limit.
Good
Feasible, and within 0.2% of the best known cost.
ETiGood
Expected time to get one good solution: time per run ÷ share of good runs.
Same code, machine and seeds for both methods. Significance: Fisher and Mann–Whitney tests.
Group OPT-09 · IA-2
8 / 13
Notes: How did we test it fairly? We used all 11 feed-mill instances from the original paper’s data set. For each instance and each method we did 3 random seeds with 20 runs each, so 60 runs per method per instance. That is 1,320 runs in total, plus 440 extra runs for the ablation tests I will show later. Both methods use the same code, the same computer and the same seeds. Only the starting points, the polish and the restart rule differ. Three measures. Feasible: the run ends without breaking any limit. Good: feasible and within 0.2 percent of the best known cost. ETiGood: the expected time to get one good solution, which is the time per run divided by the share of good runs. To check that the gains are not luck, we used two statistical tests: Fisher’s exact test on counts of good runs, and the Mann–Whitney test on the final cost gaps.

## Slide 9: Results: more good answers, faster
96%
of runs end feasible
Up from 88% with random starts (mean of 11 instances).
33.9%
good runs on the 6 hard instances
Up from 6.4%. The paper reports 14.8%.
5.0×
shorter time to a good solution
Over 5 of the 6 hard instances. Over all instances with good runs: 2.0×.
Mean over all 11 instances: good runs rise from 43.6% to 62.0%.
Group OPT-09 · IA-2
9 / 13
Notes: Now the results. First, reliability: with our method 96 percent of runs end feasible, up from 88 percent with random starts. Second, quality: on the six hard instances, 33.9 percent of runs are good, up from 6.4 percent. The original paper reports 14.8 percent, so we beat the paper too on average. Third, speed: the expected time to get a good solution is 5 times shorter on the hard instances where both methods find one. That is five of the six; on af-6-f our method found no good run, so it is left out. If you include every instance where both methods find a good run, the speed-up is 2 times, because on easy instances our method is slower. Over all 11 instances, good runs rise from 43.6 to 62.0 percent. Each run of our method costs about 19 percent more time, but far fewer runs are wasted.

## Slide 10: Good answers on the hard instances
IA-1: random restarts
IA-2: our method
% of runs that are good
af-2
1.7%
68.3%
af-3
1.7%
31.7%
af-4
20.0%
58.3%
af-6-fs
3.3%
26.7%
af-7
10.0%
18.3%
af-6-f
1.7%
0.0% (not solved)
Paper (SLP-CPLEX): af-2 19.4% · af-3 20.0% · af-4 19.8% · af-6-fs 5.2% · af-7 20.4% · af-6-f 4.0%
Group OPT-09 · IA-2
10 / 13
Notes: This is the same result instance by instance, for the six hard ones. Orange is random restarts, blue is our method. On af-2, good runs go from under 2 percent to 68 percent. On af-4, from 20 to 58. On af-3, from under 2 to 32. On af-6-fs, from 3 to 27. On af-7 there is a smaller gain, from 10 to 18. On af-6-f, the hardest one, our method found no good run, and I will say that honestly on the limits slide. At the bottom you can see what the paper reports for its own method. We are above the paper on af-2, af-3, af-4 and af-6-fs, and slightly below it on af-7 and af-6-f.

## Slide 11: Every part of the method helps
NOT JUST LUCK
5 of 11
instances with significantly more good runs (Fisher, p < 0.01)
9 of 11
instances with significantly lower final cost gaps (Mann–Whitney, p < 0.01)
GOOD RUNS (%), SEED 12345, 20 RUNS EACH
Instance | IA-1 baseline | Polish only | Smart start + polish | Full method
af-2 | 0% | 0% | 20% | 65%
af-3 | 0% | 0% | 5% | 15%
af-4 | 25% | 25% | 25% | 60%
Polish mainly fixes feasibility. Smart starts add variety. The learning search adds the big gains.
Group OPT-09 · IA-2
11 / 13
Notes: Is this just luck, and do we need every part? On luck: we used two statistical tests. For good runs, Fisher’s test says the gain is significant, with p below 0.01, on 5 of the 11 instances. For the final cost gap, the Mann–Whitney test says our method is better, again with p below 0.01, on 9 of the 11. On the parts: we tested the method in pieces, using seed 12345 and 20 runs each. Polish alone mostly fixes feasibility but barely changes the share of good runs. Smart starts plus polish help, for example af-2 goes from 0 to 20 percent. The full method, with the learning search, gives the big gains: 65 percent on af-2, 15 on af-3, 60 on af-4. So the parts complement each other: smart starts give variety, and the learning search gives depth. A fair caveat: our runs inside one seed depend on each other, so the tests slightly overstate the sample size. That is why we used three seeds and also checked each seed separately.

## Slide 12: Honest limits
af-6-f is not solved
Neither method reaches the good zone: IA-2 0%, IA-1 1.7%, paper 4.0%.
Easy instances get slower
The extra LPs make the time to a good solution up to about 2× worse.
af-7 stays just below the paper
18.3% good runs, against 20.4% in the paper.
More reliable, not always best
On af-4 one IA-1 run found the exact best known cost; our best run is 0.19% above it.
Also: 3 × 20 runs against 500 in the paper, a different LP solver (HiGHS instead of CPLEX), and the diet bound is tight only on af-1.
Group OPT-09 · IA-2
12 / 13
Notes: We want to be clear about what our method does not do. First, af-6-f, which is the paper’s af-6, is still not solved: no run of ours reached the good zone, and the baseline reached it once in 60 runs. Second, on easy instances the extra LPs cost time, so the time to a good solution can be up to about 2 times worse. Third, on af-7 we are slightly below the paper: 18.3 against 20.4 percent. Fourth, on af-4 one baseline run found the exact best known cost, while our best run is 0.19 percent above it. So our method is more reliable, but not always better in the single best run. Also, we used 3 times 20 runs while the paper used 500, we used a different LP solver and computer, and our lower bound is tight only on af-1. We also chose our parameters once, on the same instances we report, which is another limitation.

## Slide 13: Structure-aware restarts make SLP reliable on hard feed-mill problems.
CONCLUSION
96%
of runs feasible (was 88%)
33.9%
good runs on hard instances (was 6.4%)
5.0×
shorter time to a good solution
Next: more seeds or 500 runs, adaptive choice between smart starts and learning moves, parallel tests, stronger lower bounds, bin capacities.
Thank you. Questions?
Group OPT-09 · IA-2
13 / 13
Notes: To conclude. The model and the SLP solver stayed exactly as in IA-1. We only changed what happens around them: smart starts, LP repair and polish, and a search that learns from the best solution so far using regret. With that, 96 percent of runs end feasible, up from 88. On the hard instances, good runs rise from 6.4 to 33.9 percent, and the expected time to a good solution is about 5 times shorter. The price is some extra time per run, and one instance, af-6-f, is still unsolved. Next steps: more seeds or the full 500 runs, choosing adaptively between smart starts and learning moves, running the tests in parallel, stronger lower bounds, and extending to bin capacities. Thank you, and we are happy to take questions.